## Slide 1: Pyregence Fuel Models

## Slide 2: Overview
Litter+duff:
  Sample Depth
FWD (1-100h)
  Sample tally
  Particle diameter (0-7.62)
CWD
  Sample tally
  Particle diameter (>7.62)
Understory veg
  Veg presence (T/F)
  Veg height (# occupied strata)
Saplings
  Plot tally
Trees
  Plot tally

## Slide 3: Litter + Duff description
Statistical model
Neg. Binomial response
  Depth at sample point
Fixed effects
  Drought mortality level
Random effects
  Gaussian process (fine-scale, spatial)
  Plot (coarse, aspatial)
Fuelbed simulation
Simulate responses (litter+duff depths) on 0.5m resolution grid in 1 or 2 dimensions
Use van Wagtendonk allometric eqns to map from depth (cm) to biomass (Mg/ha)

## Slide 4: Litter+duff reality check
Rounding depth to nearest integer to use NB response
Litter+duff depth combined
Subsample level

## Slide 5: FWD description
Statistical Models
Tally at sample
  Neg. Binomial response
    Tally on 1m subtransect
  Fixed effects
    Drought mortality level
  Random effects
    Gaussian process (fine-scale, spatial)
    Plot (coarse, aspatial)
Particle size
  Inv-Gamma response
  Truncated to [0, 7.62]
  Fixed effects
    Drought mortality level
Fuelbed simulation
Simulate tally of 1-100h on 1m resolution grid in 1 or 2 dimensions
For each simulated particle, simulate a diameter, then bin them into 1h, 10h, 100h size classes
  Arbitrary size bins possible
Use van Wagtendonk allometric eqns to map from tally in size class (#) to biomass (Mg/ha)

## Slide 6: FWD reality check
Plot-level means
Subsample level

## Slide 7: CWD description
Statistical Models
Tally at sample
  Poisson response
    Tally on 1m subtransect
    NB failed to fit
  Fixed effects
    Drought mortality level
  Random effects
    Gaussian process (fine-scale, spatial)
    Transect (orientation bias)
    Plot (coarse, aspatial)
Particle size
  Inv-Gamma response
  Truncated to [>7.62]
  Parameters vary by drought mortality level
Fuelbed simulation
Simulate tally of CWD on 1m resolution grid in 1 or 2 dimensions
For each simulated particle, simulate a diameter
Use van Wagtendonk allometric eqns to map from sum of squared diameters (cm2) to biomass (Mg/ha)

## Slide 8: CWD reality check

## Slide 9: Understory veg description
Statistical Model
Presence/Absence of vegetation at sample
  Bernoulli response
  Fixed effects
    Drought mortality level
  Random effects
    Gaussian process (fine-scale, spatial)
    Plot (coarse, aspatial)
Count of occupied strata at sample
  Binomial response
    N occupied 0.25m strata, counting up from ground level to a max of 3.5m
  Fixed effects
    Drought mortality level
  Random effects
    Gaussian process (fine-scale, spatial)
    Plot (coarse, aspatial)
Fuelbed simulation
Simulate vegetation presence on 0.5m resolution grid in 1 or 2 dimensions
Simulate vegetation height on identical grid, filter to only points where veg is present
  0.5m =~ mean crown diameter in McGinnis sample
Assume each pixel with height >0m is an individual plant with crown volume = height*pi*(0.25^2)
Use generic McGinnis equation for biomass ~ crown vol
Assume each pixel with height >0m is an individual plant with diameter = 0.56m and height h
  Crown area = 1 pixel = 0.25m2; similar to midpoint crown area in McGinnis of 0.3m2 from midpoint diameter of 0.62m
Use generic McGinnis equation for biomass ~ diameter + height
Divide total biomass into the occupied 0.25m strata

## Slide 10: Understory veg reality check

## Slide 11: Understory veg reality check

## Slide 12: Understory veg reality check

## Slide 13: Trees and saplings model description
Neg. Binomial response
  # of trees in plot
Fixed effects
  Drought mortality level
Simulate total count of trees from a NB with mean scaled to plot size
Assign random locations within the simulation space
Use Jenkins equations to get biomass in stem, bark, foliage
  And branches = total – stem – bark – foliage
Use allometric equations to estimate crown radius, voxelize using assumption of conical stem, conical/cylindrical crown